## Slide 1
Lancet: Research
NEW TECH
LANCET TYPES
Genteel (USA)
Vacuum + vibration, no squeezing. FDA-cleared, reusable.
WATCH
Product Rsrch
ERBILITE laser (NSL, Moscow)
Laser lances the finger. needle-free, 6 depth levels. Clinic device.
WATCH
Leech-style suction cup (ETH Zurich)
Suction + ~12 microneedles, ~195 µL (animal). Seeking partners.
INNOVATION CANDIDATE
Product Rsrch
Pressure-activated
Press on finger — fires automatically
Push-button
Remove tab, press button
Side-button
Press side trigger — least intuitive
Microneedles
Suction Cup

## Slide 2
Lancet: Top Contenders
30G × 1.8
lowest pain
28G × 1.8
26G × 1.8
23G
21G × 2.0
most blood
Maker
Gauge × depth
Activation
Est. price/pc
Product photo
Unistik 3 Extra
Owen Mumford, UK
dsmedical.co.uk
21G × 2.0 mm
Side button
₹11
Accu-Chek Safe-T-Pro Uno
Roche
apollopharmacy.in
pre-set 1.5 mm
Push button
₹5–9 (est.)
Accu-Chek Safe-T-Pro Plus
Roche
midmeds.co.uk
23G, 1.3 / 1.8 / 2.3 mm
Push button, adjustable
₹15–25 (est.)
SteriLance NEW
SteriLance, China (OEM)
en.sterilance.com
23–30G × 1.8 mm
Pressure + button
₹3–6 (est.)

## Slide 3
Blood Transfer: 7 Device Types
Squeezable pipette
Manual
User controls volume
Inverted cup
Automatic
5 µL, 170M+ in malaria kits
Calibrated pipette
Semi
Fill to the mark
Capillary tube
Semi
Users underfill
Straw
Manual
Draw and blow out
Loop
Manual
Picks up a droplet
Conical cup TOP
Automatic
~23 µL, 92% vs 74% fill
space for photos

## Slide 4
Pipette: Top Contenders
01
Conical Cup
FIND
~23 µL capillary
Touch-to-fill
pmc.ncbi.nlm.nih.gov
NEW
02
UniSampler-type
Affimedix / generics
Fixed volume
Locks into vial
Affimedix
LAUNCH
03
Minivette POCT
Sarstedt
10–200 µL
Piston + stop filter
sarstedt.com
BENCHMARK
04
Microsafe
Safe-Tec
Fixed volume
One-piece, drop-free
cliawaived.com
BENCHMARK
05
Absorptive tip
Mitra, Trajan
10–30 µL in 2–4 s
neoteryx.com
NEW TECH